## Slide 1: DRC Waiver Request
M15313

## Slide 2: M2.DN.1

## Slide 3: M2.DN.1 (1)
325 u
138 u
Error | Achieved Density (Mininum density inside red areas) | Required Density in 75um X 75um
M2.DN.1 | 0.4% | 10%
This is the Capacitance Array for one SAR ADC located on the top of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.

## Slide 4: M2.DN.1 (2)
Error | Achieved Density inside Red area | Required Density in 75um X 75um
M2.DN.1 | 6.5% | 10%
This is the Capacitance Array for one SAR ADC located on the middle right of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.
500 u
260 u

## Slide 5: M3.DN.1

## Slide 6: M3.DN.1 (1)
325 u
138 u
Error | Achieved Density (Mininum density inside red areas) | Required Density in 75um X 75um
M3.DN.1 | 0.4% | 10%
This is the Capacitance Array for one SAR ADC located on the top of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.

## Slide 7: M3.DN.1 (2)
Error | Achieved Density inside Red area | Required Density in 75um X 75um
M3.DN.1 | 2.7% | 10%
This is the Capacitance Array for one SAR ADC located on the middle right of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.
500 u
260 u

## Slide 8: M4.DN.1

## Slide 9: M4.DN.1 (1)
325 u
138 u
Error | Achieved Density (Mininum density inside Red areas) | Required Density in 75um X 75um
M4.DN.1 | 0.5% | 10%
This is the Capacitance Array for one SAR ADC located on the top of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.

## Slide 10: M4.DN.1 (2)
Error | Achieved Density inside Red area | Required Density in 75um X 75um
M4.DN.1 | 1.3% | 10%
This is the Capacitance Array for one SAR ADC located on the middle right of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.
500 u
260 u

## Slide 11: M7.DN.1

## Slide 12: M7.DN.1 (1)
325 u
138 u
Error | Achieved Density (Mininum number inside Red areas) | Required Density in 75um X 75um
M7.DN.1 | 0.46% | 10%
This is the Capacitance Array for one SAR ADC located on the top of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.

## Slide 13: M7.DN.1 (2)
Error | Achieved Density (Mininum density inside Red areas) | Required Density in 75um X 75um
M7.DN.1 | 7.4% | 10%
This is the Capacitance Array for one SAR ADC located on the middle right of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.
500 u
260 u

## Slide 14: M8.DN.1

## Slide 15: M8.DN.1 (1)
325 u
138 u
Error | Achieved Density (Mininum Density inside Red areas) | Required Density in 75um X 75um
M8.DN.1 | 0.4% | 20%
This is the Capacitance Array for one SAR ADC located on the top of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.

## Slide 16: M8.DN.1 (2)
Error | Achieved Density inside Red area | Required Density in 75um X 75um
M8.DN.1 | 5.4% | 20%
This is the Capacitance Array for one SAR ADC located on the middle right of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.
500 u
260 u

## Slide 17: M8.DN.1 (3)
Error | Achieved Density inside Red area | Required Density in 75um X 75um
M8.DN.1 | 0% | 20%
This is the Capacitance Array for one SAR ADC located on the middle left of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.
154 u
180 u

## Slide 18: M8.DN.1 (4)
Error | Achieved Density (Mininum number inside Red areas) | Required Density in 75um X 75um
M8.DN.1 | 17% | 20%
This is the Capacitance Array for one SAR ADC located on the bottom of the chip. The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.
424 u
264 u

## Slide 19: M9.DN.2

## Slide 20: M9.DN.2
Error | Achieved Density (Mininum number inside Red areas) | Required Density in 75um X 75um
M9.DN.2 | 0% | 20%
This is the Capacitance Array for the four SAR ADCs The Cap array is very sensitive to the dummy fill which will worse the ADC’s performance. Dummy exclude layers are put around Cap array.