## Slide 1
ECE 266 Lab3 Design Review
Mingjie Ma
Chengming Li
University of California, San Diego, La Jolla, CA, USA

## Slide 2: uCAP Layout
2.5u
2.52u
Layer: M1 to M7 stack up
Size: 2.5u by 2.52u
CC: 5fF

## Slide 3: Schematic-singleDAC(cap bank)
Dummy

## Slide 4: Metal Width vs. Current
How much current we need?
  Q = CV
How wide of the trace should be?(Read from PDK doc)
  M1(0.4um): 0.57 mA
  M2 – M7 (0.4um): 0.72 mA
  M2 – M8 (0.8um): 1.47 mA

## Slide 5: singleDAC(cap bank) Floorplan – Common Centroid
Bit | B0 | B1 | B2 | B3 | B4 |  |  |  |  | 
CC(fF) | 10.14 | 21.8 | 44.04 | 58.25 | 101.5 |  |  |  |  | 
Ratio |  | 2.145 | 2.02 | 1.322 | 1.74 |  |  |  |  | 

## Slide 6: singleDAC(cap bank) Floorplan
Bit | B0 | B1 | B2 | B3 | B4 |  |  |  |  | 
C+CC(fF) | 6.4994 | 12.333 | 23.683 | 45.248 | 86.676 |  |  |  |  | 
Ratio |  | 1.898 | 1.920 | 1.910 | 1.916 |  |  |  |  | 

## Slide 7: RCX Cap Table
Example:
Bot7
C: 86.5f F
CC:
1)Top 679.49f F
2)Bot6: 27.7 f F

## Slide 8: Layout - singleDAC – Bit0123 - center
76.74u
121.97u
Non-symmetry
Bit 0:3 (M1, M3, M5, M7) overlapping

## Slide 9: Layout - singleDAC – Remove2Dummy
Pro:
Symmetry
Less CC between Bits and
Less CC effects to the Dummy for bit0
Cons:
Sensitive to C(w.r.t substrate)
Sensitive to the length of Bit 0:3
Non-binary routing

## Slide 10: Layout - singleDAC – Robust C+CC
76.74u
121.97u
Improvement:
Higher metal used for M0:3
Binary routing
Robust C+CC sensitivity

## Slide 11: RCX Cap Table
Bit | B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8
C+CC(fF) | 7.819 | 14.36 | 28.755 | 56.594 | 106.62 | 210.30 | 413.19 | 812.55 | 1574.86
Ratio |  | 1.84 | 2.00 | 1.97 | 1.88 | 1.97 | 1.96 | 1.97 | 1.94

## Slide 12: Appendix – Old Version uCap