## Slide 1
ECE 283 Lab3 Design Review
Mingjie Ma
Chengming Li
University of California, San Diego, La Jolla, CA, USA

## Slide 2: MotherBoard + DaugtherBoard
Modularized the Design
  By having jumper between each IC
Testability
  Jumper for GND for easy probeing
  Grab & Probe
Configurability
  Potentiometer for tweaking the perfect Vcm, AVDD, AVDDESD

## Slide 3: MotherBoard + DaugtherBoard BringUp TestPlan

## Slide 4: Current Issue 1.0
Period: 1u s
Freq; 1M Hz
CLK_IN
Connect the CLK onto the board
1MHz, 0.5V Offset, 1 Vpp

## Slide 5: Current Issue 1.1
Then connect the sine wave on to the board
500kHz, 0V offset, 500m Vpp
Sin_IN drags the CLK frequency downs to 500KHz
CLK_IN

## Slide 6: Current Issue 1.2 However…
We tried Mingjie’s Lab instrument
Everything looks good as expected
Had saved all the probes, function generator, oscilloscope, and power supply setup.
Will give another attempt on Wednesday in our 266B’s Lab
SE_DE_POS: 0.5V offset, 0.5Vpp
CLK_IN: 0.5V offset, 1Vpp

## Slide 7: Current Issue 2
Some distortion @ 10MHz CLK_IN
Adding lots of noise on SIN IN

## Slide 8: Current Issue 3 - SEDE
Different DC offset after SE-DE
But similar Vpp Amplitude
SE_DE_POS
SE_DE_NEG

## Slide 9: FFT – one of SINE
-15 dBV @ fundamental frequency
Other tones are below -70 dBV

## Slide 10: ADC_Test_Questions
What data needs to be saved to plot SNR, THD, etc…
  Digital code file from oscilloscope
  FFT Data from oscilloscope
  what else?