## Slide 1
ECE 283 Lab3 Final Design Review
Mingjie Ma
Chengming Li
University of California, San Diego, La Jolla, CA, USA

## Slide 2: Agenda
Project Background & Introduction
Specs Overview
Chip Design Review in Cadence
Chip-Testing Review
Takeaway

## Slide 3: Project Background & Introduction

## Slide 4: Project Background & Introduction
ECE266A - 9-bit high speed(Fs = 10M Hz) SAR ADC
  Layout-focus Design
    Comparator, CDAC, Digital logic, Non-overlapping clock generator, switches
  Mega-Chip combinations
    4 groups of chip into one BIG CHIP
    Dummy fill, seal ring, custom pads, custom-DeCaps, wavier submission
ECE266B – SAR ADC Testing
  PCB Design
    Mother(4-Layer) and daughterboard(2-Layer) combination
    Custom ADC chip footprint + Wirebonding Diagram
  Soldering & Assembly
    0604 & 0802 Surface mount soldering
  Device characterization & Test - Automation
    Test Automation using Keysight instruments in Python
    Data processing and plotting in MatLab

## Slide 5: Specs Overview

## Slide 6: Specs Overview
Speces | Performance
@ 1kHZ | 50.23 dB
@ 1kHZ | 61.45 dB
@ 1kHZ | 50.68 dB
@ 1kHZ | 78.36 dB
@ 1kHZ | 61.45 dB
Speces | Performance
 | 50.23 dB
 | 61.45 dB
 | 50.68 dB
 | 78.36 dB
 | 61.45 dB

## Slide 7: Chip Design Review in Cadence

## Slide 8: Comparator Remarks
Symmetry layout in differential pair
Achieved 90uV offset in the differential pairs

## Slide 9: Custom unit Cap Remarks
2.5u
2.52u
Layer: M1 to M7 stack up
Size: 2.5u by 2.52u
CC: 5fF

## Slide 10: CDAC Remarks -1
78.69u
125.5u

## Slide 11: CDAC Remarks -2
Bit TopP | B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8
CC(fF) | 5.51874 | 11.0181 | 21.9972 | 44.1238 | 88.179 | 176.362 | 352.691 | 705.664 | 1413.44
Ratio |  | 1.9996 | 3.9859 | 7.9952 | 15.9781 | 31.9569 | 63.9080 | 127.866 | 256.116
Bit TopN | B0 | B1 | B2 | B3 | B4 | B5 | B6 | B7 | B8
CC(fF) | 5.51138 | 11.0222 | 21.9988 | 44.1662 | 88.2156 | 176.425 | 352.801 | 705.712 | 1413.26
Ratio |  | 1.9998 | 3.9915 | 8.0136 | 16.0060 | 32.0110 | 64.0131 | 128.046 | 256.425

## Slide 12: Chip-Testing Review

## Slide 13: MotherBoard BlockDiagram
Low Pass Filter()
LPF
Buffer
Jumper
SE-DE
Jumper
SIN_P
SIN_P
SIN_N
Buffer Signal (Maintain drive strengthen)
Single-ended to Differential Ended
SMA
SIN_N
SMA
Bypass- Method
Bypass- Method
SE/DE- Method
CLK

## Slide 14: MotherBoard + DaugtherBoard 3D

## Slide 15: MotherBoard + DaugtherBoard
Modularized the Design
  By having jumper between each IC
  For debugging
  SE-DE / ByPass Options
Testability
  Jumper for GND for easy probeing
  Grab & Probe
Configurability
  Potentiometer for tweaking the perfect Vcm, AVDD, AVDDESD
4-Layer Stack
  Signal
  DGND + AGND
  +5V
  -5V

## Slide 16: Board Bring-up Checklist
By knowing what to expect after each IC
Actual vs. Expect
Handy to debug the problem

## Slide 17: Test Setup Documentation

## Slide 18: Test Automation Setup - 1
Power Supply
  +5V, -5V, and 2.5V
Function Generator
  CLK & SIN INPUT
Oscilloscope
  Digital Analyzer
  Digital Output
4-Layer Stack
  Signal
  DGND + AGND
  +5V
  -5V

## Slide 19: Test Automation Setup - 2
Power Supply
  +5V, -5V, and 2.5V
Function Generator
  CLK & SIN INPUT
Oscilloscope
  Digital Analyzer
  Digital Output
4-Layer Stack
  Signal
  DGND + AGND
  +5V
  -5V
2.5V -5V +5V
SIN_P & SIN_N
CLK_IN
C0-C8 + EOC

## Slide 20: Test Automation Code Prep
Keysight Connection Expert & Keysight Command Expert
  Extremely accelerate the code development time
  And check if the instrument is there
Python Test Automation
  Function Generator
    Freq_coupling', 'FuncGenConnect', 'Load__setup', 'PWM_setup', 'Polarity_invert', 'Sin_setup', 'Sync_phase', 'UnitVpp_setup', 'Voltage_coupling', 'output_OFF', 'output_ON
  PowerSupply
    'Channel_Select', 'Current_Setup', 'Output_OFF', 'Output_ON', 'PowerSupply_Connect', 'Voltage_Setup'
  Oscilloscope
    'DigitalDisplay_ON', 'Digitalizer_ON_OFF', 'Oscilloscope_Connect', 'Oscilloscope_RUN', 'Oscilloscope_SetBUS', 'Oscilloscope_Single', 'Oscilloscope_Stop', 'Oscilloscope_TimeBase', 'Oscilloscope_Trigger_Dchan', 'Oscilloscope_Trigger_External', 'Oscilloscope_WGen_Square', 'Oscilloscope_WGen_Square_OFF', 'Oscilloscope_WGen_Square_ON', 'Save_waveform', 'SetDigital_Threshold’
Code Version Control
  GitHub
    Never lost what I did on “Yesterday”

## Slide 21: Peak SNDR Plot
Speces | Performance
@ 1kHZ | 50.23 dB
@ 1kHZ | 61.45 dB
@ 1kHZ | 50.68 dB
@ 1kHZ | 78.36 dB
@ 1kHZ | 61.45 dB
Speces | Performance
 | 50.23 dB
 | 61.45 dB
 | 50.68 dB
 | 78.36 dB
 | 61.45 dB

## Slide 22: Peak SNDR Plot

## Slide 23: Future Work
Improve the code to make coherent sampling using:
  By adjusting the input frequency
  By grabbing enough cycles, no more no less (ideally prime number)
  By grabbing data points
Rework the mother and daughter board
  Putting more decaps to filter-out the noise
  Make it to be plugging-in and direct-use Eval-Board

## Slide 24: Takeaway

## Slide 25: Takeaway
Always Always Always document everything
Simple Eval-board Design = Robust Debuggability & Reconfigurality
Cross-check everything with partners

## Slide 26: Acknowledgement
Prof. Hall
  For running this 6-months course/projects
  Helping us debug the problems
TA: Darshan
  Supporting the Lab work
  Extending the Lab Hours
Apple
  For sponsoring this projects, buying the chips, PCBs, components,etc
Keysight
  Instruments, instrument command & connection expert